        Wave structure

Let's consider the scheme for constructing the “rain” effect. Raindrops are members of a numbered structure/object called drop. The maximum number of <DR_Quan> droplets on a tape of length ,<LEN_all> for STM8S103 with a clock frequency of 16 MHz can reach ten. The drop object consists of two parts: 1. -flash (trace from the fall), this is just a bright dot <bright> with a duration of <T_spl> cycles, time and place of occurrence - <t_app, x_app> 2). - a colored wave, diverging in both directions, with a lifetime T_life. The wave has 3 parameters - time, location <vert> and amplitude <w_max>. The "thickness" of the wave is chosen to be constant - 5-6 points. The amplitude of the wave decreases over time from <bright> at the moment <t_app> to 0 at the moment <T_life>. The brightness of points near the maximum of the wave <vert> decreases exponentially depending on the distance to <vert>. The structure of the wave is shown in Fig. 1 .